## Slide 1: PHYVOS: Physical Layer Voting for Secure and Fast Cooperation
Bocan Hu, Yan Zhang, and Loukas Lazos
Department of Electrical and Computer Engineering,
University of Arizona
IEEE CNS 2015, Florence Italy
Notes: Add committee Members

## Slide 2: Cooperation in Distributed Wireless Networks
Distributed wireless networks rely on the cooperation principle to coordinate network functions
Scalability, availability, fault-tolerance, cost-efficiency
E.g.,
Cooperative diversity in spectrum sensing for opportunistic networks
Spectrum sensing period is specified to 2 sec [IEEE 802.22]
f1
f2
f3
f4
FC
legacy user

## Slide 3: Cooperation in Distributed Wireless Networks
Distributed wireless networks rely on the cooperation principle to coordinate network functions
Scalability, availability, fault-tolerance, cost-efficiency
E.g.,
Coordination in networked multi-agent systems
Consensus delay specified in msec range

## Slide 4: Simplest From of Coordination
Exchange of state information – equivalent to a “yes/no” voting process
A set of actors u1, u2 ,…, uM cast M binary votes v1, v2 ,…, vM
E.g., γ = 0 implements a plurality rule
Voting outcome
threshold
actor votes
u1
u3
u2
FC

## Slide 5: Secure Message-Based Voting
A sequential process that scales linearly with the number of voters
Additional delay overhead to guarantee integrity
Voter authentication and message integrity
Delay is further amplified for coordination of channel access
time
PHY
header
MAC header
1-bit vote
signature or HMAC
v1
v2
v3
v4
Notes: However, current voting mechanisms rely on sequential message based voting that scales linearly with the number of voters. In the example here four votes are submitted sequentially. For binary voting, each vote consists of a PHY header a MAC header and a 1-bit vote.
For secure voting additional delay overheads are incurred. For instance, a signature may need to be included with every vote to verify the voter identity and the vote integrity.
The voting delay is amplified if voters have to contend for channel access.

## Slide 6: PHYVOS: PHY Layer-Based Voting Scheme
A simultaneous process that minimizes the communication and delay overhead
Robustness: Voting outcome reflects the true outcome in the presence of external attacks and malicious voters
time
PHY
header
MAC header
1-bit
vote
signature or HMAC
Notes: We developed a PHY-layer voting scheme called PHYVOS, which is designed to implement secure voting at far smaller delay. PHYVOS transforms the voting process form a sequential one to a simultaneous one, where all voters cast their votes at the same time.
It also eliminates the need for PHY headers, MAC headers and signatures.
We have shown the robustness of the voting outcome form external attacks and malicious voters.

## Slide 7: Simultaneous Vote Casting
time
time
time
time
Fusion Center
f5
f4
f3
f2
f1
f0
f5
f4
f3
f2
f1
f0
v1
v2
v3
Exploit the subcarrier orthogonality of OFDM
OFDM symbols at the receiver
Notes:   The idea of simultaneous vote casting is as follows.
  - Each voter has two designated subcarriers.
  The voter casts a vote v_i by adding energy on one of the two subcarriers (several symbols are used for a single vote). The subcarrier index is selected based on the vote value and a pseudorandom sequence shared between the voter and the fusion center.
  The fusion center receives OFDM symbols composed of the OFDM signals of all the voters. It then applies energy detection on each subcarrier, at the outtput of the FFT without demodulating the OFDM symbols received.
  The heart of the security of the system lies on the pseudorandom sequence shared between the voter and the FC as well as the fact this it is particularly challenging to erase energy from a channel.

## Slide 8: Vote Casting Phase
Each actor ui is assigned two subcarriers fj and fj+1
The FC and ui share random binary sequence based on some pairwise seed si
Ri(si) = { ri(n) = PRNG(n, si), n = 1,2, . . . }
To cast vi, actor ui casts l symbol votes in either fj or fj+1 by transmitting l OFDM symbols
ay, k = j + vi XOR ri(n)
xk(n) =
0, otherwise
E.g., Ri(si) = { 1, 0, 0, 1 },
time
random symbol
f1
f2
vi = 1
Notes:   Exactly what the slides sais.

## Slide 9: Voting Tallying Phase
The FC computes the vote of each actor and tallies the votes
subcarrier
. . .
Energy
v1
vN-1
.
.
.
No demodulation
f0
f1
f2
f3
f4
f5
fn-2
fn-1
threshold
v0
Notes:   In the vote tallying phase the FC computes the voting outcome.
  Looking at the design of the OFDM receiver, this is done by measuring symbol energy on each subcarrier after the FFT transform but before demodulation. Then a threshold is applied to detect the subcarriers that contain votes.
  The subcarrier indexes are XORED with the secret PRNG sequence of each voter to extract the actual vote. This process is repeated for several symbols.

## Slide 10: Adversary Model
Injects OFDM signals to change the voting outcome T
Does not launch DoS attack (i.e., a voting outcome must be computable)
Secret vote model: Adversary is unware of the voting intent of each actor
Open vote model: Adversary is aware of the voting intent of each actor
u1
u3
u2
Notes:   -> A mobile distributed storage system consists of a community of mobile devices that are capable of storing data.
  -> A File F is stored within a geographically limited area A
  -> The user downloads data from the community devices rather than from the infrastructure network.
  -> Thus, it eases the traffic on the infrastructure network.

## Slide 11: Modification of a Single Vote
Adversary injects energy on one of the subcarriers to swing or nullify a vote
time
FC
time
time
f1
f0
f1
f0
f1
f0
+
adversary
voter
Notes:   To modify a single vote, the adversary can add energy to a channel to indicate a different vote. Take for example an adversary attacking a voter that is assigned subcarriers f1 and f2. Because the voter varies the channel he uses for casting a symbol vote based on Ri, the adversary has to guess which subcarrier to use to convey a particular vote value.
  As this is a random guess, for some slots he conflicts with the casted vote and with some he reinforces the vote.
  Note that it is very hard for the adversary to systematically erase energy from a channel. The transmitted symbol is not known ahead of time, and the channel between the voter and the FC cannot be easily measured from another location.
  So at best, the adversary can hope to nullify a vote, which happens with probability 0.5^l. This is just l successes over l Bernoulli trials. So by increasing the number of symbol votes that constitutes a vote, we can drive the probability of vote nullification at any value,

## Slide 12: Modification of the Voting Outcome
Secret vote model:
δ: # of attacked votes μ: winning margin
M: # of voters, γ: decision threshold (e.g., γ = 0)
p: Pr[vi = e], n1: (M+γ+μ)/2
Open vote model:
YES
We can select the number of symbol votes to drive the above probabilities to any desired value
NO
γ
μ
δ
Notes:   Using the vote nullification probability, we can compute the probability of modifying the vote outcome for the secret and open vote models, which is expressed by the following two propositions.
  In the calculation of these probability, we have assumed M voters, a vote decision threshold of gamma, a margin mu (number of positive votes over gamma), and the number of votes attacked by the adversary (delta)

## Slide 13: Robustness for the Secret Vote Model
20 voters, plurality vote, adversary attacks δ = N/2 + μ votes
Notes:   This plot shows the voting outcome robustness for different number of symbol votes per vote and different margin votes. Using this plot we can choose lambda to achieve a desired robustness degree.
  For example, we can select ell to be equal to 12 to guarntee robustness with probability 10^-3

## Slide 14: Robustness for the Open Vote Model
20 voters, plurality vote, adversary attacks δ = N/2 + μ votes
Notes: A similar process can be followed for the open vote model, but a slightly higher number of symbol votes is used to guarantee the same security level. This is because the adversary focuses only on positive votes.

## Slide 15: Voting Overhead
MV: message-based voting using 802.11g (52 subcarriers, 6 bits per symbol, 13 symbol gap between messages)
DMV = 20 M – 13 OFDM symbols
PHYVOS: up to 26 votes can vote
simultaneously using l OFMD symbols
DPHYVOS = ceil (M/26)
PHY
header
MAC header
1-bit
vote
HMAC
CRC
5
30
4
32
1
Notes: We also compared the delay overhead of a message based voting scheme with PHYVOS.
Then what the slide says.

## Slide 16: Frequency Synchronization
Carrier frequency offset (CFO) effect on demodulation:
Subcarriers are not orthogonal, causing ICI
Symbols at each subcarrier appear with arbitrary rotation in the constellation map
PHYVOS:
No preamble is present to perform CFO synchronization
No demodulation necessary, so constellation point rotation does not affect vote tallying
No ICI as long as freq. misalignment stays below subcarrier spacing
In 802.11g subcarrier spacing is 315Khz while CFO is < 100 KHz

## Slide 17: Time Synchronization
Time misalignment: propagation delay and device clock drifts. Cyclic prefix (0.8 μsec) is applied to normal OFDM symbol.
Increasing the CP to account for synchronization error.
Cast a symbol vote in two symbol durations.

## Slide 18
4 NI USRP 2921 devices
Carrier frequency: 2.4 GHz
# of subcarriers: 64
Configurations
Topology A: equidistant
Topology B: varying distances
PHYVOS Implementation on USRPs

## Slide 19
Selection of Vote Detection Threshold
Three voters assigned at 1st, 5th and 9th subcarrier casting 1,000 votes using BPSK modulation
Topology A: voters are placed 5 ft from FC
Topology B: voters are placed 5/10/15 ft from FC

## Slide 20
MAC for Multi-channel Networks ( MMAC)
Received Power Per Subcarrier
Detection threshold set to -80dBm
Topology A
Topology B

## Slide 21
MAC for Multi-channel Networks ( -MMAC)
Voting in the Presence of an Adversary
Voter 1 assigned 1st and 2nd subcarrier
Voter 2 assigned 5th and 6th subcarrier
Adversary injected energy to subcarriers at random
Topology A
Topology B

## Slide 22: Concluding Remarks
Contributions Summary
Designed a PHY-layer based voting scheme for fast coordination
Voting is performed without explicit message exchange
Significantly lower communication and delay overheads compared to message based voting
Robust to vote manipulation without expensive cryptography
Future Work
PHYVOS robustness and correctness under varying channel conditions
Extend PHYVOS to accommodate x-ary voting
Investigate the application of PHY-layer voting to fully distributed consensus algorithms (No Fusion Center)

## Slide 23: Thank you!