## Slide 1: Thwarting Inside Jamming Attacks on Wireless Broadcast Communications
Sisi Liu, Loukas Lazos, and Marwan Krunz
Dept. of Electrical and Computer Engineering
University of Arizona
WiSec 2011, Hamburg, Germany

## Slide 2: Roadmap
Jamming of broadcast communications
Time delayed broadcast scheme (TDBS) – single hop topologies
Time delayed broadcast scheme – multi-hop topologies
Security and performance evaluation
Final Remarks

## Slide 3: Jamming of the Wireless Medium
Open nature of wireless medium leaves it exposed to Jamming
Jamming: Deliberate interference with radio transmissions in order to decrease SNR and corrupt signal beyond recovery
Sender
Receiver
Jamming

## Slide 4: Conventional Anti-Jamming Techniques
Spread-spectrum (SS) communications
Adversary has to spread his energy on a large bandwidth
slot 1
slot 2
slot 3
slot m
f1
f2
f3
f4
l1
l4
l2
li: location of transmission at slot i
PNi
PNi
Notes: Unfortunately, spread spectrum communications can provide anti-jamming protection only to the extent that the PN sequence remains secret.

## Slide 5: Extending SS to Broadcast Communications
PNi
PNi
PNi
PNi
PNi
PNi
PNi
PNi

## Slide 6: Broadcast Communications in Wireless Networks
Omni-directional antennas – Broadcast advantage
  A single transmission can reach multiple receivers
  Energy and bandwidth efficient
  Extensively used to disseminate control information
Impact of Broadcast Jamming on Wireless Networks
s
infrastructure-based: Cell broadcasting, paging, synchronization
ad-hoc: bootstrapping, channel access, routing

## Slide 7: Problem Statement - Contributions
Problem:
Develop anti-jamming methods for broadcast communications
Internal threat model – compromise of network devices
Contributions:
Propose a frequency hopping (FH) technique for broadcasting
Map the FH design to 1-factorization problem in complete graphs
Show resilience to jamming under node compromise
Eliminate common secrets such as PN codes, keys, etc.

## Slide 8: Relevant Work – Internal Jammer Model
Uncoordinated Frequency Hopping (UFH) [Pöpper et al, JSAC 2010]
Uncoordinated Direct-Sequence SS [Pöpper et al, Usenix 2009]
Randomized Differential DSSS [Liu et al, Infocom 2010]
Tree-based keying schemes for identifying inside jammers [Chiang and Yu, Infocom 2008]

## Slide 9: Time-Delayed Broadcast Scheme (TDBS)
A series of unicast transmissions
spread over frequency and time
f2
Time slot: 1 2 3 4 5
n1
n2
n3
n4
n5
n1
n2
n1
n3
n1
n4
n5
n1
n1
n5
f3
f4
f1
x

## Slide 10: TDBS – Design Motivation
  Concurrent unicasts on multiple frequencies
  Jammer can only block a fraction of the transmissions
Trade delay and energy efficiency for jamming resilience
Differences with classical FHSS systems
  Each node is assigned a unique PN sequence
  Compromise of a subset of PN sequences limits the information leakage with respect to uncompromised ones
Other design aspects
  Fairness, delay minimization
How to design hopping sequences?
Notes: And the location of the unicast as we showed in the last page is defined by a frequency/slot pairs

## Slide 11: Some Definitions
1-factorization
1-factor
Definitions
  Complete graph K2n(V, E): each pair of vertices in V is connected by an edge
  1-factor F: a set of pairwise-disjoint edges that cover V (matching)
  1-factorization F2n: A series of (2n - 1) factors F2n = {F0, F1 ,…, F2n-2} that span the edge set E
  Theorem: Complete graphs are 1-factorable
K4

## Slide 12: Mapping to the 1-factorization Problem
For each 1-factor, randomly assign frequency bands to each pair
set of nodes in broadcast group
communicating pair
Slot:
h1:
h2:
h3:
h4:
f2
f2
f3
f3
f3
f4
f4
f3
f1
f5
f1
f5
f5
f3
f3
f5
f3 . . .
f1 . . .
f3 . . .
f1 . . .
1 2 3 4 5
1
2
3
4
1
2
3
4
1
2
3
4
F0:
F1:
F2:
f2
f3
f3
f4
f1
f5

## Slide 13: TDBS – SU: Sequential Unicast Mode
Sender sequentially relays information
to intended receivers
Applicable to infrastructure-based nets
f2
Time slot: 1 2 3 4
n1
n2
n3
n4
n5
n1
n2
n1
n3
n1
n4
n1
n5
f3
f4
f1
K: number of channels
2n: number of nodes

## Slide 14: Properties of the SU mode
1-factorizations guarantee that every node will meet every other node in (2n - 1) slots
Compromise of a node reveals the rendezvous of that node
F0 | F1 | F2 | F3 | F4 | F5 | F6 | F0 | F1 | F2
1 8 | 1 2 | 1 3 | 1 4 | 1 5 | 1 6 | 1 7 | 1 8 | 1 2 | 1 3
2 7 | 3 8 | 4 2 | 5 3 | 6 4 | 7 5 | 8 6 | 2 7 | 3 8 | 4 2
3 6 | 4 7 | 5 8 | 6 2 | 7 3 | 8 4 | 2 5 | 3 6 | 4 7 | 5 8
4 5 | 5 6 | 6 7 | 7 8 | 8 2 | 2 3 | 3 4 | 4 5 | 5 6 | 6 7
Slot: 1 2 3 4 5 6 7 8 9 10

## Slide 15: TDBS–AB: Assisted Broadcast Mode
Any node that receives a broadcast message acts as a broadcast relay
Applicable to ad hoc based nets
n1
n2
n3
n4
n5
f2
Time slot: 1 2 3
n1
n2
n1
n3
n3
n5
f3
f4
f1
n2
n4
K: number of channels
2n: number of nodes

## Slide 16: Constructing FH Sequences for the AB Mode
Relay set of node j: set of nodes that can relay a transmission originating from j
Goal: Maximize for every j and every 1-factor

## Slide 17: Resilience to External Jammers – SU Mode
Random Jammer
  E[D]: Expected delay for the completion of a broadcast
  p: J/K fraction of channels jammed by adversary

## Slide 18: Resilience to External Jammers – AB Mode

## Slide 19: Resilience Under Node Compromise
Jammer has compromised nodes (FH sequences become known)
Uncertainty with respect to the FH sequences of legitimate nodes is reduced
E[D] until legitimate nodes receive a broadcast message
AB mode
SU mode

## Slide 20: Extension to Multi-Hop Networks
Cluster-based network architecture: Clique clustering
Intra-cluster slots
Inter-cluster slots
Interleave

## Slide 21: Intra-cluster phase
Divide set of frequencies to 4 sets
Apply 4-color theorem
Construct FH sequences for the nodes within each cluster (AB or SU mode)

## Slide 22: Inter-cluster phase
Cluster labeling: Clusters with same color transmit on the same slot
Create bipartite graphs between gateway nodes (break ties, merge)
Assign random permutation of frequencies to edges
4
7,8
2
9,10
3
11, 12
14
15,18
5
6,13
16
17
18
cluster A
cluster D
f2
f11
f22
f33
f8
f25

## Slide 23: Evaluation of Multi-hop Scenario
Security metrics
Nc : # of adjacent clusters on average
NL :# of “bridge links” between two adjacent clusters
E[Df]
E[De]
E[DIV]

## Slide 24: Evaluation of Multi-hop Broadcasting

## Slide 25: Final Remarks
Developed Time-delayed Broadcast Scheme
  Anti-jamming scheme for broadcast communications under internal threat model
  Trades delay and communication efficiency with jamming resilience
  Realizes broadcast as a series of unicasts distributed in frequency and time
  Uses a mapping to 1-factorization of complete graphs to improve resilience while reducing delay
Future TDBS features
  Dynamic addition and deletion of broadcast group members
  Investigation of FH adjustment for collision avoidance among neighboring clusters
  FH resynchronization in case of synchronization loss