## Slide 1: Security Vulnerability and Countermeasures of Frequency Offset Correction in 802.11a Systems
Hanif Rahbari, Marwan Krunz, and Loukas Lazos
Department of Electrical & Computer Engineering
University of Arizona
INFOCOM 2014

## Slide 2: Jamming Wireless Communications
Bob
Jamming: intentional interference with radio transmissions
Alice
hdr
payload
Jamming models: constant, random, reactive, frame-selective
Models differ in hardware, energy requirements, complexity, stealthiness, effectiveness
Jay

## Slide 3: Jamming Efficiency - Duration
Jamming duration (τj) for dropping a packet
  A function of coding, data rate (modulation), interleaving, jamming power, …
hdr
payload
τj: 10% - 20% of a frame, BER ~ 5% - 10%
τj: 0.5% of the frame, BER ~ 50%
Frequency Offset (FO) attack
  Targets the part of the preamble used for FO estimation
  Independent of coding scheme, data rate, etc.
τj
τj

## Slide 4: Frequency Offset (FO) in OFDM Systems
Frequency Offset (FO): The difference in operating freq. between two devices
OFDM systems (802.11a/g/n, …) are very sensitive to FO
Zero ICI
FO
Frequency domain: OFDM subcarriers w/o FO
Frequency domain: OFDM subcarriers w/ FO
Non-zero ICI

## Slide 5: 802.11a Preamble
FO is estimated from the PHY preamble (publicly known)
Δfs = 4 Δf
f
1
5
9
Subcarrier spacing of STSs and LTSs
Δfl = Δf
1
2
3
f
f
Related to the FO amount that can be corrected
STS Spacing
LTS Spacing
Notes: Only jam STSs

## Slide 6: FO Estimation (Noiseless)
conjugate
Same sample
transmitted after t
ith sample
Phase offset
ri
ri+t
ri
*
FO
ri+t
ri
ri+t
t

## Slide 7: FO Estimation (Noisy)
Because of noise, the estimation is erroneous
  : an estimate of in the presence of noise
To better estimate , a summation of ’s is used
t

## Slide 8: FO Estimation Limits
Estimated phase offset is limited to
Estimated FO:
FO is unambiguous as long as f ≤ 0.5 * subcarrier spacing
  STS can correct up to 2Δf LTS can correct up to 0.5Δf
Rx first uses STSs for coarse FO estimation (less samples)
LTS are used for FO estimation refinement (more samples)
Δfs = 4 Δf
f
1
5
9
1
2
3
f
f
Δfl = Δf
STS Spacing
LTS Spacing

## Slide 9: FO Estimation and Correction (Example)
An OFDM system with 4 subcarriers
  1) Estimate using STSs
  2) Estimate using LTSs
Bob
Alice
Receiving
Correct after STSs
Correct after LTSs
1
2
Notes: Assume Alice transmits exactly at the nominal frequency.
During STSs, only one subcarrier is active

## Slide 10: FO Estimation Attack
Principle: Alter the estimated FO beyond the correctable range of LTSs by jamming STSs
Phase differences as seen during STSs:
To correct FO after STSs
Jamming is successful if
Correctable phase offset range by LTSs
Notes: Delude Bob into incorrectly estimating the FO during STSs such that the resulting correction after STSs is not fixable during LTSs.

## Slide 11: FO Estimation Attack (Example)
Alice
Receiving
Correct (STSs)
Correct (LTSs)
00110110
01
11
00
10
01
11
00
xx
Bob
xx 00 11 01 
00 11 01 10 
xx xx xx xx  ~0.5 BER
Channel estimation errors due to large FO during LTSs
Notes: Correct FO = 40%

## Slide 12: Step 1: Impose a Desired Phase Offset
Use a jamming signal u with the same structure as STSs
For STS + jamming samples:
(1) scalar
(3) Unknown amplitude
& unknown phase
(2)
known phase
(1)
(2)
(3)
Eve-Bob FO
Notes:   Δ𝜑_𝐸: Eve to Bob phase offset
  Υ : a complex coefficient
  Besides the actual FO between Eve and Bob, Eve can add an artificial FO to the jamming signal to create a total FO of Δ𝜑_𝐸 at Bob
Assume that Eve precisely detects the beginning of the frame.
\delta f_ab is known
Eve is unable to control ∠𝑩 because 𝑟 and 𝑢 are channel dependent and hence, unknown
  I.e., the last two terms in 𝑩 are unknown

## Slide 13: Step 1: Impose a Desired Phase Offset (con’d)
To control , the jammer first has to eliminate the effect of the channel-dependent term urY
Rearrange

## Slide 14: Step 2: Elimination of Channel-Dependent Term
Define the second jamming sample u2 as a function of the first sample u1 to eliminate the effect of urY (pairing rule).
Preamble samples at the Tx

## Slide 15: Step 3: Selection of Injected Offset
B is simplified to one scalar and one complex variable with controllable phase
Multiply samples of ui with any desired phase to inject desired offset at the Rx
For sample i of ui -> Multiply with
is the additional FO to ensure obtains any desired value
Additional optimizations w.r.t. jamming power |ui|2

## Slide 16: Evaluation (Simulations)
Worst case:
Demodulated into wrong subcarriers: random bits
Correct bits (no demodulation error)
Demodulated into wrong bits but possibly correctable
Corresponding constellation maps of data symbols
Estimated by STSs
BER after LTSs
Notes: Rotation because of channel estimation errors
Implemented in LabVIEW
Parameters
  1) 𝛿𝑓_𝐸: Eve’s FO
  2) Signal-to-Jamming ratio
Metrics:
  1) Coarse FO estimation error
  2) Channel estimation MSE
  3) BER
Assumptions
  AWGN channel
  Accurate frame detection

## Slide 17: Final Remarks
We have demonstrated fast frame detection and accounted for timing imperfections: https://www.youtube.com/watch?v=WAumaL0YOJE
We have optimized the attack w.r.t jamming power
Demonstrated the FO attack on USRPs
Preliminary Defenses
Sequence hopping (SH)
  To estimate this FO, nonadjacent sequences (up to two STSs away) are sufficient
  Randomly select two STSs from all the STSs
Preamble obfuscation: modify the preamble structure at the Tx
Example: Tx artificially changes the FO of the preamble according to some pre-agreed rule, not known to the jammer
1
2
3
4
5
10
9
8
7
6

## Slide 18: Frame Detection (Symbol Timing)
1st window
2nd window

## Slide 19: Experimental Evaluation
NI-2921 USRPs
  5GHz band
  Connection through Gigabit Ethernet NIC
Eve
Alice
Bob

## Slide 20: Step 3: Optimizing the Jamming Power
Successful attack
region
Eve to Bob FO

## Slide 21: Experimental Evaluation (con’d)
Estimated FO after LTSs
  deb: Eve-to-Bob to Alice-to-Bob distance ratio (equivalent to SJR)
  Sequence Hopping (SH) is often successful in mitigating the FO attack
The jammer is successful even if he has a longer distance to the RX
Successful attack: One shift forward
Successful attack: Two shifts backward
Notes: A USRP is not capable to switch from Rx to Tx fast enough
Our remedy: Detect a packet, jam the next one
  Alice transmits at fixed intervals of 𝑇 milliseconds
  Eve need to react in less than 4 microseconds once she detects a frame
  The best reaction time of USRPs is shown to be 15 microseconds

## Slide 22: Step 4: Accounting for Synchronization Errors
1
2
5
4
7
6
3
8
9
10
13
12
15
14
11
16
Jamming seed
Notes: Blue edges (dependencies) are due to pairing rule while green edges are due to chaining rule