## Slide 1: Countering Selfish Misbehavior in Multi-channel MAC protocols
Yan Zhang and Loukas Lazos
Dept. of Electrical and Computer Engineering
University of Arizona
INFOCOM 2013

## Slide 2: Channel Access in Multi-channel Wireless Networks
A - D
B - E
C - F
A
B
D
E
F
C
F - D
A - B
E - C
C - A
B - F
D - E
F - C
B - A
E - D
f1
f2
f3
collision domain
Multiple Tx - Rx pairs within same collision domain share access to a common set of frequency bands
  Schedule-based
  Contention-based
Notes:   Before we go to multi-channel MAC protocols, let’s look into the channel access problem in multi-channel wireless networks.
  2 ways to allocate common resource to multiple pairs: schedule-based where various xmissions are scheduled in freq. and time.
  Contention-based allocation. In such mechanism, nodes contend for allocation of available freq. bands in distributed manner.
  An example here, 6 nodes within collision domain, 3 available freq. bands. By coordinating channel access among multiple pairs, we want to ensure various transmissions can take place in parallel over 3 channels without collisions.

## Slide 3: Prior-Art on Multi-Channel MAC (MMAC) Protocols
  Design goals
    Allow transmitters to discover the residing frequency of receivers
    Maximize throughput (aggregate, individual)
    Ensure fairness
  Dedicated control channel designs
    Nodes equipped with multiple radios one of which is always tuned to the control channel
  Frequency hopping rendezvous designs
    Nodes rendezvous at different channels via hopping - no contention
  Split-phase designs
  Single half-duplex transceiver is assumed
Notes:     Typically, channel access problem is dealt at MAC layer. A lot of work has been done on designing Multi-channel MAC protocols, referred to as MMAC.
    First of all, MMAC needs to allow xmitters to discover… Second, MMAC needs to maximize…Also, MMAC needs to ensure fairness, which means that everyone has a fair access opportunity.
    To classify existing works, there are 3 types of MMAC.
    Dcc: Nodes are equipped with multiple radios. One of the radios is always tuned to control channel in order to reserve data channel for communication, after reservation, another radio is switched to reserved channel to perform data transmission.
    FH: nodes ren…via hopping, two nodes can communicate upon rendezvous. A FH design typically has no contention phase.
    Split-phase: time divided alternating cp and dp. single half-duplex…since nodes cannot listen and xmit at same time, they converge to a default cc during cp to reserve a channel and discover the residing freq. of other node in upcoming dp…then when dp arives, they switch to reserved channels to exchange data simultaneously.
    Our work focus on split phase MMAC.

## Slide 4: Problem Statement
  MMAC protocols effectively coordinate access if contenders are benign and protocol-compliant
  Misbehavior in MMAC Protocols
    What if nodes behave selfishly to gain an unfair share of the available channels?
    What are the possible misbehaviors and optimal misbehavior strategies?
    What is the misbehavior impact on throughput and fairness?
    How can this misbehavior be mitigated?
    Can misbehaving nodes be identified?
A-D
B-E
C-F
A-D
C-B
E-F
A-D
B-F
C-E
A-D
B-C
E-F
f1
f2
f3
A-D

## Slide 5: Our Contributions
  We study possible misbehaviors in split-phase MMAC designs
    Backoff Manipulation Attack (BMA)
    Multi-Reservation Attack (MRA)
    Combination of both attacks
  We derive adaptive misbehavior strategies for isolating a desired subset of channels
  We develop misbehavior mitigation methods that provide fair channel access opportunities
  We develop misbehavior detection methods that identify the misbehaving nodes
Notes:   Nodes must discover the channel where other nodes reside

## Slide 6
f1
RES
PCLB | 
f1 | MED
f2 | MED
f3 | MED
PCLB | 
f1 | LOW(1)
f2 | MED
f3 | MED
PCLB | 
f1 | LOW(1)
f2 | LOW(1)
f3 | MED
PCLB | 
f1 | LOW(1)
f2 | LOW(1)
f3 | HIGH
reservation request
acknowledgment
response
Reservations are placed based on a three-way handshake
Channel selection criteria: balance traffic load - Preferable Channel List (PCL)
REQ
REQ
REQ
ACK
ACK
ACK
RES
RES
RES
C- F
F(f1)
A
B
C
C(f1)
D(f2)
E(f3)
A(f2)
B(f3)
Control Phase
Data Phase
A
B
D
E
F
C
MAC for Multi-channel Networks ( MMAC)
Split-Phase MMAC Design
REQ
ACK
f2
f3
A-D
B-E
f1
f2
f3
Notes: There could be many criteria when selecting a channel. Here we use the best criteria which is balance traffic load for channel selection.
Traffic load is recorded through maintaining priority for each channel in a PCL.
Also, since data phase is much longer than the duration of single packet transmission, nodes are allowed to place rsvs with different destinations to improve throughput.

## Slide 7: Backoff Manipulation Attack (BMA)
Node A systematically selects small backoff values to capture the control channel (similar to misbehavior in single-channel MAC protocols)
Solutions from the single-channel domain cannot be directly ported
  Backoff monitors may disperse to multiple channels
  Sender-monitor pair may collude (e.g., if monitor is a receiver)
REQ
REQ
ACK
ACK
RES
RES
C-F
A
C
D(f2)
F(f1)
A(f2)
C(f1)
Control Phase
Data Phase
A
B
D
E
F
C
A-D
f1
f2
f3
Notes: From now, I’ll introduce the attacks we have identified in the paper. The first type is BMA. This is actually known from the single-channel MAC protocols.
Suppose A is a misbehaving node, it systematically selects …Because control channel usually has a limited duration, when the number of contending nodes is large, some of them may not have the chance to access control channel. In this case, if A repeats launching BMA, it can
Consistently seize the control channel in every control phase.
Many solutions for single-channel BMA have been proposed, where… However, they cannot be directly be ported.

## Slide 8: Multi-reservation Attack (MRA)
Reservations with fictitious nodes
I1, I2, and I3 are presumed to be hidden terminals to
nodes B to F
REQ
REQ
ACK
ACK
RES
RES
F(f1)
A
C
C(f1)
D(f2)
A(f2)
Control Phase
A
B
D
E
F
C
C - F
f1
f2
I1
I2
I3
ACK(f2)
ACK
ACK
ACK
A(f2)
A(f2)
A(f2)
fake reservations
REQ
ACK
RES
B
E(f1)
B(f1)
Data Phase
f1
f2
B - E
C - F
B - E
PCLB | 
f1 | MED
f2 | MED
PCLB | 
f1 | MED
f2 | LOW(1)
PCLB | 
f1 | MED
f2 | LOW(4)
PCLB | 
f1 | LOW(1)
f2 | LOW(4)
PCLB | 
f1 | HIGH
f2 | LOW(4)
A - D
A - D
A - D
A - D

## Slide 9: MRA – Incomplete Negotiations
C
D
B
A
REQ(PCLA)
ACK(f1)
REQ(PCLA)
ACK(f1)
PCLD | 
f1 | MED
f2 | MED
PCLD | 
f1 | LOW(1)
f2 | MED
Notes: The PCL of D is distorted due to these incomplete negotiations

## Slide 10: Misbehavior Throughput Advantage in BMA+MRA
20ms control phase
(about 8 negotiations/phase )
30ms control phase
(about 12 negotiations/phase )
Simulation setup (OPNET)
  Single-hop network, 10 well-behaved pairs, 1 misbehaving pair
  3 orthogonal channels of 2Mbps, data phase: 80ms
  Poisson distributed traffic with parameter λ
Notes: contention window fixed to 4, send out 5 fake reservations to isolate 1 of the 3 channels.
The first figure shows the throughput of nodes as a function of lambda when control phase is set to 20ms. Two scenarios are simulated: one is no misbehavior scenario, and the other is scenario with misbehavior. As we can see, when traffic load is fairly low, the misbehaving node does not gain any advantage, while as traffic load increases, nodes need to contend, and the misbehaving node is able to gain significant advantage over well-behaved nodes.

## Slide 11: Adaptive Misbehavior Strategy
To isolate nm out of n channels:
Step 1: Place nm reservations on nm channels of choice
Step 2: Allow for (n - nm) reservations from other pairs
Step 3: Repeat Steps 1 and 2
E.g., n = 3, nm = 1
reservations from
misbehaving node
RSVW
RSVW
RSVW
RSVM
RSVM
RSVW
……
reservations from
well-behaved nodes
RSVM
RSVW
PCLX | 
f1 | MED
f2 | MED
f3 | MED
PCLX | 
f1 | LOW(1)
f2 | MED
f3 | MED
PCLX | 
f1 | LOW(1)
f2 | LOW(1)
f3 | LOW(1)
PCLX | 
f1 | LOW(2)
f2 | LOW(1)
f3 | LOW(1)
PCLX | 
f1 | LOW(2)
f2 | LOW(2)
f3 | LOW(2)
Notes: I am not reaching the math details, but in our paper, we proved that only … are needed to ensure a misbehavior node to …

## Slide 12: Evaluation of Adaptive Misbehavior
Adaptive strategy requires significantly less reservations than
placing a fixed # of reservations a priori
collisions
d: fixed # of reservations for guaranteeing isolation of one channel

## Slide 13: Detection of BMA – Backoff Generation Module
number of retransmissions
G
si
seed
G(qi, si) in [0,1]
Node i publishes a random seed si used to compute its random backoff times
qi: packet #
Backoff for the qith packet from i

## Slide 14: Detection of BMA – Backoff Monitoring Module
Control Phase
Data Phase
f1
f2
f3
REQ (1,0)
ACK
RES
(1,0)
RTS
(2,0)
CTS
DATA
ACK
Monitored backoff
< bI(1,0) ?
Monitored backoff
< bi(2,0)?
Transmitting node includes (qi, ri) with every control packet transmitted during the control and data phases
Monitoring nodes keep track of (qi, ri) and identify misbehaving nodes based on
bi (qi, ri)
Notes: Nodes publish a public random sequence for computing random backoff times.
Include parameters (qi,ri) with every control packet transmitted during
control and data phases
Monitoring nodes keep track of (qi,ri) and compute bi (qi,ri)
Identify misbehaving nodes that adopt smaller backoff values based on their public schedules

## Slide 15: Manipulation of (qi, ri)
Scenario A: Misbehaving node i avoids incrementation of (qi, ri) if its REQ collides
Collisions are receiver-dependent – another neighbor may have successfully received REQ(qi, ri)
A
B
F
C
D
REQ(qA, rA)
Scenario B: Misbehaving node i takes advantage of other collisions to advance qi by k (k > 1), with G(qi + k, si) << G(qi,+1 si)
With the advancement of q by k, r must also advance by k.
Delay for k collisions/backoffs must be added to backoff delay
Notes: Nodes publish a public random sequence for computing random backoff times.
Include parameters (qi,ri) with every control packet transmitted during
control and data phases
Monitoring nodes keep track of (qi,ri) and compute bi (qi,ri)
Identify misbehaving nodes that adopt smaller backoff values based on their public schedules

## Slide 16: Mitigation of MRA – Modified PCL Rules
ACK
ACK
RES
RES
F(f1)
A
C
C(f1)
D(f2)
A(f2)
Control Phase
A
B
D
E
F
C
f1
f2
I1
I2
I3
ACK(f2)
ACK
ACK
ACK
A(f2)
A(f2)
A(f2)
fake reservations
ACK
RES
B
E(f2)
B(f2)
PCLB | 
f1 | MED
f2 | MED
PCLB | 
f1 | MED
f2 | LOW(1)
PCLB | 
f1 | LOW(1)
f2 | LOW(1)
PCLB | 
f1 | LOW(1)
f2 | HIGH
A source can change the priority of a channel at most once per control phase
Misbehaving node A does not isolate f2
ATIM
ATIM
ATIM
Notes: Explain how to change pcl rule: further check packet generator;
We want to further detect fictitious source and so that misbehaving node can be identified

## Slide 17: Mitigation of MRA – Secure Neighbor Discovery
Discover 2-hop topology and record hidden terminals
F is hidden terminal to all but M  M is suspected of misbehavior
Execute challenge-response between A and F
Detecting fictitious sources
F
M
A
B
D
C
Topological information
n: direct neighbor, h: non-direct neighbor
Notes: Each node I creates a parent list for each of its two-hop neighbors (j). The parent list contains the set of nodes which are i’s 1-hop neighbor, and also

## Slide 18: Effect of Mitigation Techniques

## Slide 19: Conclusions and Future Work
Studied the impact of misbehavior on split-phase MMAC protocols
Derived adaptive misbehavior strategies which are able to monopolize
a desired subset of channels
  Future work
  Investigate misbehavior strategies for dedicated control channel
  and frequency hopping MMAC designs
  Couple misbehavior detection with a reputation system
  Proposed detection/mitigation schemes that identify misbehaving nodes and further provide fair channel access opportunities

## Slide 20
Thank you!