## Slide 1: FD-MMAC: Combating Multi-channel Hidden and Exposed Terminals Using a Single Transceiver
Yan Zhang, Loukas Lazos, Kai Chen,
Bocan Hu, and Swetha Shivaramaiah
Electrical and Computer Engineering
University of Arizona
INFOCOM 2014

## Slide 2: Channel Access in Multi-channel Wireless Networks
A - D
B - E
C - F
A
B
D
E
F
C
F - D
A - B
E - C
C - A
B - F
D - E
F - C
B - A
E - D
f1
f2
f3
A set of nodes within the same collision domain share access to fixed number of channels
  Schedule-based
  Contention-based
Notes:   In this work, we address the problem of improving throughput and delay efficiency of distributed multi-channel MAC protocols.
  Before we go to multi-channel MAC protocols, let’s look into the channel access problem in multi-channel wireless networks.
  2 ways to allocate common resource to multiple pairs: (1) schedule-based where various transmissions are scheduled in freq. and time.
  (2) Contention-based allocation. In such mechanism, nodes contend for allocation of available freq. bands in distributed manner.
  As an example here, 6 nodes within collision domain, we have 3 available freq. bands here. By coordinating channel access among multiple pairs, various transmissions can take place over the 3 channels in parallel without collisions.
  This function is typically achieved by multi-channel MAC protocol.

## Slide 3: The Multi-channel Hidden Terminal Problem
RTSA
CTSB
PA
A
B
C
hidden
terminal to A
A
B
C
f1
C switches to f1
t0
t1
t2
t3
collision
backoff
RTSC
Notes:     There are several challenges in designing a multi-channel MAC protocol. The first challenge is the multi-channel hidden terminal problem. Suppose A wants to communicate with B on channel f1, and C is a hidden terminal to A. A and B first perform RTS-CTS exchange, after which A transmits a data packet PA to B, let’s say PA begins at time t0 and ends at t1. If during transmission of PA, C also switches to f1 at time t2. In this case, C misses the chance to hear CTS and thus determines f1 to be idle because it is out of A’s transmission range. After proper backoff, C also initiates an RTS to B at time t3, which causes a collision at B.

## Slide 4: The Multi-channel Exposed Terminal Problem
RTSB
CTSA
PB
A
B
C
exposed
terminal to B
A
B
C
f1
C switches to f1
t0
t1
t2
D
C defers transmission
Notes:     The second challenge is the multi-channel exposed terminal problem. Suppose node B wants to communicate with A on f1, and C is an exposed terminal to B. To communicate, B and A first perform RTS-CTS exchange, after which data packet PB is transmitted. Suppose C switches to f1 during PB’s transmission, C is not able to know it is in exposed terminal location due to missing RTSB. As a result, C defers its transmission to D due to sensing the transmission of PB.
    (On a single channel, node C can identify itself as an exposed terminal to B if it only hears RTS but not CTS. However, when there are multiple channels, C may not be able to know this information.)
    There are also other challenges in designing multi-channel MAC, such as destination discovery and load balancing. I will talk about how we address these problems in detail later.

## Slide 5: Prior-Art on Multi-channel MAC (MMAC)
Split-phase designs (SP-MMAC)
Frequency hopping rendezvous designs (FH-MMAC)
REQ
REQ
REQ
ACK
ACK
ACK
RES
RES
RES
Data
control phase
data phase
Data
Data
f1
f2
f3
Dedicated control channel designs (DCC-MMAC)
REQ
REQ
REQ
ACK
ACK
ACK
RES
RES
RES
Data
Data
Data
f1
f2
f3
Notes:     Krunz: “For SP-MMAC, control phase fixed duration is not really a limitation for MMAC, control phase can be adjusted.”
    Common disadvantages of DCC-MAC and SP-MMAC: 1. Use of control channel decreases spectral efficiency; 2. Control channel saturation; 3. Control channel single point of failure.
    SP-MMAC: a node needs to wait for next control channel if (1): the node does not successfully reserve a channel during control phase, or (2) a node changes its destination in the middle of a data phase.
    FH-MMAC: does not address the hidden/exposed terminal problem.

## Slide 6: Full-Duplex Multi-Channel MAC (FD-MMAC)
  Design a distributed MMAC protocol that:
    Eliminates the use of a control channel
    Combats the multi-channel hidden terminal problem
    Reduces control signaling
    Improves spectral efficiency by enabling the operation of
    exposed terminals
    Achieves load balancing and fairness autonomously
Notes:   Split-phase:

## Slide 7
MAC for Multi-channel Networks ( MMAC)
PA
BCNB
ACKB
A
B
A
B
PHY
MAC
PA
tACK
te
BCNB
PHY
CRC
IDB
tACK
BCNB:
BCNB
BCNB
BCNB
Communication in Full-Duplex (FD) Mode
Notes: The FD operation mode is one of the key ideas of our FD-MMAC protocol. This example shows how nodes utilize FD to communicate in FD-MMAC.

## Slide 8
MAC for Multi-channel Networks ( MMAC)
A
B
PA
BCNB
CO
TO
RO
CO: Collision region
- No packet decodable due
to collision of PA with BCNB
C is only allowed to transmit in TO region
TO: Transmitter-only region
- PA decodable
- Exposed terminal
RO: Receiver-only region
- BCNB decodable
- Hidden terminal
C
C
C
FD Carrier Sensing
Notes: Here is how region is classified regarding to an ongoing transmission A-B. To achieve this region classification, one practical issue is how to efficiently evaluate decodability of data packet.

## Slide 9
MAC for Multi-channel Networks ( MMAC)
BCN=Yes
A
B
PA
BCNB
CO
TO
RO
C1
C2
C3
C4
Use EVM measurement to
differentiate TO from CO
capture effect
Capture effect: C may have a low EVM at C2
Use RSS to differentiate C1 from C2
If RSS is beyond threshold,
C assumes it is in the CO
Use BCN decodability to
differentiate RO from TO/CO
BCN=No
BCN=No
EVM < γEVM
EVM > γEVM
RSS < γRSS
BCN=No
EVM < γEVM
RSS > γRSS
Region Classification Rules
Notes: Incorporating the EVM measurement, we are able to set the region classification rules.
Nodes have lower EVM in TO/RO region compared with CO region.
Another practical issue is capture effect.

## Slide 10
MAC for Multi-channel Networks ( MMAC)
C
hidden
terminal to A
A
B
PA
BCNB
A
B
C
C switches to f1
t0
t1
t2
defer
PHY
MAC
PA
sense
ACKB
BCNB
BCNB
BCNB
BCNB
t
(f1)
Combating Multi-channel Hidden Terminals
Notes: With FD carrier sensing, multi-channel hidden terminals are practically eliminated.
By decoding BCNB, C infers itself in RO region and defers from transmission
In case BCNB cannot be decoded, C is expected to have high EVM, C then infers itself
in CO region and still defers from transmission.
C is in RO in practice, but may infer itself in CO but this is ok.
Absence of BCN packet indicates collision of PHY and MAC headers due to hidden terminal - Sender aborts further transmission and retransmit.

## Slide 11
MAC for Multi-channel Networks ( MMAC)
A
B
PA
BCNB
CO
TO
RO
C
D
PC
BCND
A
B
C
PHY
MAC
PA
ACKB
BCNB
BCNB
BCNB
D
PHY
MAC
PC
sense
backoff
C switches to f1
t2
TO region
ACKD
BCND
BCND
BCND
(f1)
(f1)
Enabling Exposed Terminal Transmissions
Notes: FD-carrier sensing also enables parallel transmission at exposed terminals.
Transmission AB occurs first
C is in the TO region of transmission AB,
thus can attempt to communicate PC to D
If D can decode the MAC header of PC, D
responds with BCND
C continues the transmission of PC upon
detecting BCND, abort otherwise
Transmissions AB and CD take place
concurrently without interfering each other

## Slide 12: RF Signal Correlation
  Detect known bit patterns in the presence of collisions
C
A
PC
B
ACKB
BCND
ACKB
PC
ACKB

## Slide 13
MAC for Multi-channel Networks ( MMAC)
Switch channel based on
Channel State Table (CST)
A contention-based, time-slotted protocol based on CSMA/CA
No control message overhead related to virtual carrier sensing
Destination’s State Diagram
Notes: Destination discovery and load balancing

## Slide 14
MAC for Multi-channel Networks ( MMAC)
f1
A
B
E
Channel State Table
at destination E
(f1)
Channel # | Idle time
f1 | tcurr
f2 | tcurr
f3 | tcurr
f4 | tcurr
E is in RO region of A-B
(BCNB decodable)
Destination Operation Example

## Slide 15
MAC for Multi-channel Networks ( MMAC)
f1
A
B
E
Channel State Table
at destination E
(f1)
Channel # | Idle time
f1 | tACK
f2 | tcurr
f3 | tcurr
f4 | tcurr
E is in RO region of A-B
(BCNB decodable)
Destination Operation Example
E updates f1’s idle time
using tACK in BCNB
(f2)
f2
C
D
E is in TO region of C-D
(cannot decode BCND)
E switches to f2 because
f2 has earliest idle time

## Slide 16
MAC for Multi-channel Networks ( MMAC)
f1
A
B
E
Channel State Table
at destination E
Channel # | Idle time
f1 | tACK
f2 | tcurr+tMTU
f3 | tcurr
f4 | tcurr
E is in RO region of A-B
(BCNB decodable)
Destination Operation Example
E updates f1’s idle time
using tACK in BCNB
(f2)
f2
C
D
E is in TO region of C-D
(cannot decode BCND)
E switches to f2 because
f2 has earliest idle time
E updates f2 ’s idle time
using worst-case estimate
E switches to f3
which is currently idle

## Slide 17
MAC for Multi-channel Networks ( MMAC)
Sender’s State Diagram

## Slide 18
MAC for Multi-channel Networks ( MMAC)
Protocol Operation Example
A
B
PA (f1)
BCNB(f1)
CO
TO
RO
D
C
PC (f1)
A
B
C
PHY
MAC
PA
D
sense
backoff
ACKB
BCNB
PHY
MAC
early termination
switch
sense
BCNB
BCNB
PHY
MAC
PC
D resides in f2
BCND
BCND

## Slide 19: Performance Evaluation
Simulation setup (OPNET)
  3 orthogonal channels of 2Mbps
  Poisson distributed traffic with parameter λ
  Protocols to compare: FD-MMAC SP-MMAC, and DCC-MMAC
  Simulated topology

## Slide 20: Aggregate Throughput – Single Collision Domain
3, 6 flows
9, 12 flows

## Slide 21: Aggregate Throughput – Exposed/Hidden Terminals
One exposed terminal
One exposed plus one hidden terminal

## Slide 22: Final Remarks
  Proposed a distributed MMAC protocol that exploits full-duplex
  communications
  Eliminates the need for a control channel
  Coordinates channel access at low control overhead
  Combats multi-channel hidden terminal problem
  Achieves destination discovery and load balancing autonomously
  Improves spatial channel reuse by enabling the operation of
  multi-channel exposed terminals

## Slide 23: Thank you!

## Slide 24
MAC for Multi-channel Networks ( MMAC)
Traditional carrier sensing
- Estimate carrier state : free vs. busy
- Defer from transmission if carrier is busy
FD carrier sensing
- Classifies a node’s location relative to an ongoing transmission
into three regions
- Determines the node’s operation state based on region
- Integrates PHY-layer techniques: Error Vector Magnitude (EVM) and Received Signal Strength (RSS) measurements
Advantages of FD carrier sensing
- Eliminates multi-channel hidden terminal problem
- Creates transmission opportunities for exposed terminals
FD Carrier Sensing
Notes: Based on the FD communication mode, we proposed a novel FD carrier sensing mechanism, which is the most critical component in FD-MMAC protocol.

## Slide 25
MAC for Multi-channel Networks ( MMAC)
- C needs to wait until PA’s transmission is completed to verify if PA can
be correctly decoded
C cannot decode PA if it switches to a busy channel in the middle of PA’s
transmission
Solution: C measures EVM values on
received symbols in order to evaluate
decodability of PA before packet reception
Transmitted symbol
Received symbol
Problems with traditional decoding method
- EVM is computed over window size n
Transmitted symbol is unknown to C
for arbitrary data packet
The symbol closest to the received
one is selected as ideal symbol when
computing EVM
Evaluating Decodability of Data Packet
Notes: When a packet is correctly decoded, the received symbols are closest to transmitted ones…(see paper)
EVM measures signal distortion due to interference or impairments on wireless channel, it is strongly related to BER.

## Slide 26
MAC for Multi-channel Networks ( MMAC)
Normalized correlation for 10 BCN packets
- PA: 500-bit payload
- BCND: 50-bit payload
C applies signal correlation
to detect BCND packets
D
C
BCND
A
PA
- DistanceC-A = DistanceC-D = 7 ft
Correlation peaks correspond
to BCND transmissions
Detection threshold = 0.005
RF Correlation Measurements

## Slide 27
MAC for Multi-channel Networks ( MMAC)
Experiment setup
  USRP devices over the 2.4GHz band
  QPSK modulation at a transmission rate of 2Mbps
  Applied phase/frequency offset correction and time sync using
  88-bit preamble sequence
A
B
PA
BCNB
CO
TO
RO
C1
C2
C3
C4
- DistanceA-B = 7 ft
- A and B transmit concurrently
- PA: 500-bit payload
- BCNB: 50-bit payload
- 100 PA and 500 BCNB
transmitted
EVM, RSS, and decodability of
BCNB are measured
Experimental Evaluation of Region Classification

## Slide 28
MAC for Multi-channel Networks ( MMAC)
EVM CDF at RO, CO, and TO regions
Average RSS at different positions
EVM and RSS Mesurements

## Slide 29: Transmission Delay
Average delay for transmitting a batch of 100 data packets