# Converting Temperatures in Celsius to Kelvin in PSpice

## Objective

Temperatures in PSpice are expressed in Celsius, but device equations depend on the thermal voltage defined in terms of the temperature in degrees Kelvin as

EQ. 1

VTH = kBT/q

where kB = Boltzmann’s constant, T = temperature in degrees Kelvin, and q = electron charge. We all have a rough idea of how to convert from  ºC to K, but a precise approach can be based on the information on the web pages:

http://physics.nist.gov/cuu/Constants/

http://www.wikipedia.org/wiki/Physical_constants

http://en.wikipedia.org/wiki/Celsius

Incorporating the results from these web pages into PSpice is accomplished by pasting a Parameter box onto the schematic, as shown in Figure 1 below.

Figure 1

Parameter box pasted into a PSpice schematic to determine the thermal voltage VTH corresponding to a temperature T_C in ºC selected as T_C = 27 ºC in this example

Conversions also can be done numerically using the on-line computation at

http://www.chemie.fu-berlin.de/chemistry/general/units_en.html

See also the conversion formulas and tables at

http://www.chemie.fu-berlin.de/chemistry/general/tscales_en.html

## Why might we need to calculate VTH?

Usually it is unnecessary to calculate VTH. However, occasionally we want to use a formula for a circuit parameter that involves the thermal voltage.

For example, we might want to compute a component value that depends upon a built-in voltage like VBE = VTH (n (IC/IS) corresponding to the base-emitter voltage of a bipolar transistor at a current IC when the scale current of the transistor is IS. We could read this voltage off a schematic for any given Q-point. But perhaps we want to avoid the necessity of typing in numbers for VBE from the schematic every time IC changes. Or, maybe we want to get a Probe sweep of circuit behavior as Q-point changes, so the component value has to be computable. In such cases, it is handy to have the Parameter box of Figure 1 available.